!-----------------------------------------------------------------
!
! Purpose
! =======
!
! LA_GESVX computes the solution to a either real or complex system of 
! linear equations  AX = B,
! where A is a square matrix and X and B are either rectangular
! matrices or vectors.
! LA_GESVX is an expert driver routine, which can also perform the
! following functions:
!    - solves   A^T X = B  or  A^H X = B,
!    - estimates the condition number of A,
!    - returns the pivot growth factor,
!    - refines the solution and computes forward and backward error
!      bounds,
!    - equilibrates the system if A is poorly scaled.
!
! Arguments
! =========
! SUBROUTINE LA_GESVX (A, B, X, AF, IPIV, FACT, TRANS, EQUED,
!                      R, C, FERR, BERR, RCOND, RPVGRW, INFO)
!    <type>(<wp>), INTENT(INOUT) :: A(:,:), <rsh>
!    <type>(<wp>), INTENT(OUT) :: <sol>
!    <type>(<wp>), INTENT(INOUT), OPTIONAL :: AF(:,:)
!    INTEGER, INTENT(INOUT), OPTIONAL :: IPIV(:)
!    CHARACTER(LEN=1), INTENT(INOUT), OPTIONAL :: EQUED
!    REAL(<wp>), INTENT(INOUT), OPTIONAL :: R(:), C(:)
!    REAL(<wp>), INTENT(OUT), OPTIONAL :: <err>, RCOND, RPVGRW
!    CHARACTER(LEN=1), INTENT(IN), OPTIONAL :: FACT, TRANS
!    INTEGER, INTENT(OUT), OPTIONAL :: INFO
!    where
!    <type> ::= REAL | COMPLEX
!    <wp>   ::= KIND(1.0) | KIND(1.0D0)
!    <rhs>  ::= B(:,:) | B(:)
!    <sol>  ::= X(:,:) | X(:)
!    <err>  ::= FERR(:), BERR(:) | FERR, BERR
!
! Description
! ===========
!
! The following steps are performed:
!
! 1. If FACT is not present or FACT = 'N', and EQUED is present, 
!    real scaling factors are computed to equilibrate the system:
!       TRANS = 'N':  diag(R) A diag(C)    inv(diag(C)) X = diag(R) B
!       TRANS = 'T': (diag(R) A diag(C))^T inv(diag(R)) X = diag(C) B
!       TRANS = 'C': (diag(R) A diag(C))^H inv(diag(R)) X = diag(C) B
!    Whether or not the system will be equilibrated depends on the
!    scaling of the matrix A, but if equilibration is used, A is
!    overwritten by diag(R) A diag(C) and B by diag(R) B (if TRANS='N')
!    or diag(C) B (if TRANS = 'T' or 'C').
!
! 2. If FACT = 'N', the LU decomposition is used to factor the
!    matrix A (after equilibration if EQUED is present) as A = PLU,
!    where P is a permutation matrix, L is a unit lower triangular
!    matrix, and U is upper triangular.
!
! 3. The factored form of A is used to estimate the condition number
!    of the matrix A.  If the reciprocal of the condition number is
!    less than machine precision, steps 4-6 are skipped.
!
! 4. The system of equations is solved for X using the factored form
!    of A.
!
! 5. Iterative refinement is applied to improve the computed solution
!    matrix and calculate error bounds and backward error estimates
!    for it.
!
! 6. If equilibration was used, the matrix X is premultiplied by
!    diag(C) (if TRANS = 'N') or diag(R) (if TRANS = 'T' or 'C') so
!    that it solves the original system before equilibration.
!
! Arguments
! =========
!
! A       (input/output) either REAL or COMPLEX square array,
!         shape (:,:), size(A,1) == size(A,2).
!         If FACT is not present or FACT = 'N',
!            On entry, the matrix A.
!            On exit, if EQUED is present, the matrix A may have been
!               overwritten by the equilibrated matrix (see EQUED).
!         If FACT is present and FACT = 'F',
!            On entry, the matrix A, possibly equilibrated in a previous
!               call to LA_GESVX (see EQUED).
!            On exit, A is unchanged.
!
! B       (input/output) either REAL or COMPLEX rectangular array, 
!         shape either (:,:) or (:), size(B,1) or size(B) == size(A,1).
!         On entry, the right hand side vector(s) of matrix B for the
!            system of equations AX = B.
!         On exit, if EQUED is present, B may have been scaled in 
!            accordance with the equilibration of A (see EQUED); 
!            otherwise, B is unchanged.
!
! X       (output) either REAL or COMPLEX rectangular array,
!         shape either (:,:) or (:), size(X,1) or size(X) == size(A,1).
!         If INFO = 0, the solution matrix X to the original
!         system of equations.  Note that X always returns the solution
!         to the original system of equations; if equilibration has been
!         performed (EQUED is present and EQUED /= 'N'), this does not
!         correspond to the scaled A and B.
!
! AF      Optional (input/output) either REAL or COMPLEX square array,
!         shape (:,:), size(AF,1) == size(AF,2) == size(A,1).
!         If FACT is not present or FACT = 'N', then AF is an output 
!            argument and returns the factors L and U from the factorization 
!            A = PLU of the original matrix A, possibly equilibrated if
!            EQUED is present.
!         If FACT is present and FACT = 'F', then AF is an input argument 
!            (and must be present); on entry, it must contain the factors 
!            L and U of A (possibly equilibrated if EQUED is present), 
!            returned by a previous call to LA_GESVX.
!
! IPIV    Optional (input/output) INTEGER array, shape (:), 
!         size(IPIV) == size(A,1).
!         If FACT is not present or FACT = 'N', then IPIV is an output 
!            argument and returns the pivot indices from the factorization 
!            A = PLU of the original matrix A, possibly equilibrated if
!            EQUED is present.
!         If FACT is present and FACT = 'F', then IPIV is an input argument 
!            (and must be present); on entry, it must contain the pivot 
!            indices from the factorization of A (possibly equilibrated 
!            if EQUED is present), returned by a previous call to LA_GESVX.
!
! TRANS   Optional (input) CHARACTER*1
!         If TRANS is present, it specifies the form of the system 
!            of equations:
!            = 'N':  A X = B    (No transpose)
!            = 'T':  A^T X = B  (Transpose)
!            = 'C':  A^H X = B  (Conjugate transpose = Transpose)
!         otherwise TRANS = 'N' is assumed.
!
! FACT    Optional (input) CHARACTER*1
!         Specifies whether or not the factored form of the matrix A is
!         supplied on entry.
!         If FACT is present then:
!            = 'N':  the matrix A will be equilibrated if EQUED is present,
!               then copied to AF and factored.
!            = 'F':  on entry, AF and IPIV must contain the factored form 
!               of A (possibly equilibrated if EQUED is present).
!         otherwise FACT = 'N' is assumed.
!
! EQUED   Optional (input/output) CHARACTER*1
!         If FACT is not present or FACT = 'N', then EQUED is an output
!            argument. If it is present, then the matrix is equilibrated,
!            and on exit EQUED specifies the scaling of A which has 
!            actually been performed:
!            = 'N':  No equilibration.
!            = 'R':  Row equilibration, i.e., A has been premultiplied
!                    by diag(R); also B has been premultiplied by diag(R)
!                    if TRANS = 'N'.
!            = 'C':  Column equilibration, i.e., A has been postmultiplied 
!                    by diag(C); also B has been postmultiplied by diag(C)
!                    if TRANS = 'T' or 'C'.
!            = 'B':  Both row and column equilibration: combines the 
!                    effects of EQUED = 'R' and EQUED = 'C'.
!         If FACT is present and FACT = 'F', then EQUED is an input 
!            argument; if it is present, it specifies the equilibration
!            of A which was performed in a previous call to LA_GESVX with
!            FACT not present or FACT = 'N'.
!
! R       Optional (input/output) REAL array, shape (:), 
!         size(R) == size(A,1).
!         R must be present if EQUED is present and EQUED = 'R' or 'B';
!         R is not referenced if EQUED = 'N' or 'C'.
!         If FACT is not present or FACT = 'N', then R is an output 
!            argument. If EQUED = 'R' or 'B', R returns the row scale 
!            factors for equilibrating A.
!         If FACT is present and FACT = 'F', then R is an input 
!            argument. If EQUED = 'R' or 'B', R must contain the row scale
!            factors for equilibrating A, returned by a previous call to 
!            LA_GESVX; each element of R must be positive.
!
! C       Optional (input/output) REAL array, shape (:), 
!         size(C) == size(A,1).
!         C must be present if EQUED is present and EQUED = 'C' or 'B';
!         C is not referenced if EQUED = 'N' or 'R'.
!         If FACT is not present or FACT = 'N', then C is an output 
!            argument. If EQUED = 'C' or 'B', C returns the column scale 
!            factors for equilibrating A.
!         If FACT is present and FACT = 'F', then C is an input 
!            argument. If EQUED = 'C' or 'B', C must contain the column 
!            scale factors for equilibrating A, returned by a previous 
!            call to LA_GESVX; each element of C must be positive.
!
! FERR    Optional (output) either REAL array of shape (:) or REAL
!         scalar. If it is an array, size(FERR) == size(X,2).
!         The estimated forward error bound for each solution vector
!         X(j) (the j-th column of the solution matrix X).
!         If XTRUE is the true solution corresponding to X(j), FERR(j)
!         is an estimated upper bound for the magnitude of the largest
!         element in (X(j) - XTRUE) divided by the magnitude of the
!         largest element in X(j).  The estimate is as reliable as
!         the estimate for RCOND, and is almost always a slight
!         overestimate of the true error.
!
! BERR    Optional (output) either REAL array of shape (:) or REAL
!         scalar. If it is an array, size(BERR) == size(X,2).
!         The componentwise relative backward error of each solution
!         vector X(j) (i.e., the smallest relative change in
!         any element of A or B that makes X(j) an exact solution).
!
! RCOND   Optional (output) REAL
!         The estimate of the reciprocal condition number of the matrix
!         A after equilibration (if done). If RCOND is less than the
!         machine precision (in particular, if RCOND = 0), the matrix
!         is singular to working precision. This condition is
!         indicated by a return code of INFO > 0, and the solution and
!         error bounds are not computed.
!
! RPVGRW  Optional (output) REAL.
!         The reciprocal pivot growth factor norm(A)/norm(U).
!         If RPVGRW is much less than 1, then the stability
!         of the LU factorization of the (equilibrated) matrix A
!         could be poor. This also means that the solution X, condition
!         estimator RCOND, and forward error bound FERR could be
!         unreliable. If factorization fails with 0<INFO<=size(A,1),
!         then RPVGRW contains the reciprocal pivot growth factor for
!         the leading INFO columns of A.
!
! INFO    Optional (output) INTEGER
!         If INFO is present
!            = 0:  successful exit
!            < 0:  if INFO = -k, the k-th argument had an illegal value
!            > 0:  if INFO = k, and k is
!               <= N:  U(k,k) is exactly zero.  The factorization has
!                      been completed, but the factor U is exactly
!                      singular, so the solution and error bounds
!                      could not be computed.
!               = N+1: RCOND is less than machine precision.  The
!                      factorization has been completed, but the
!                      matrix is singular to working precision, and
!                      the solution and error bounds have not been
!                      computed.
!         If INFO is not present and an error occurs, then the program is
!            terminated with an error message.
!--------------------------------------