SUN's Petascale Strategy: Applications driven system Architecture
based on
Open Standards and Open Source
Dr. Giri Chukkapalli, Ph.D
Sun Microsystems, Inc.

---
Architecture Optimization based on Constraints
Application
Constraints
Open
Hardware/Software
Standards
Petascale System Architecture
General
Constraints
Hardware
Constraints

---
Architecture Constraints
Application constraints in the form of performance ratios
Fundamental Hardware constraints
Open Hardware standards as much as possible
Opensource and Open standards based software
General constraints
  - TCO
  - Power, Space and Cooling
  - RAS
  - Usability, Programmability

---
Petascale Application space

---
 Petascale application space
Coupled Multi-scale Multi-physics simulations
  - wide range of algorithms can be part of a single simulation
Solving Inverse problems
  - Optimization outer loop
  - An order of magnitude more compute intensive
Solving Adjoint and other data driven simulations
  - Strong parallel file system IO requirements
Convergence of traditional and commercial HPC
ALL these trends in HPC application space have direct impact on future HPC software/Hardware industry

---
Convergence of Traditional & Commercial HPC
National HPC Centers and large scale commercial data centers
  - Similar power, space and cooling problems
Growth in reliance on HPC in Commercial space
  - Crash testing
  - Bioinformatics
  - Financial forecasts
  - Oil & Natural gas
  - Climate/Weather
HPC is one of the main growth targets

---
Petascale Algorithmic Space
Convergence of algorithms across disciplines
  - Adaptive, Multi-grid
  - Spectral element
  - Optimization of Gov. Eq. Solutions
Optimized libraries, templates and frameworks
  - FFTW,	Atlas, SPRNG
  - GA, Charm++
  - WRF
  - SUN's active support to developer communities through COE
Support of PGAS languages
Natural progression to Fortress

---
Spectral parallelism
Petascale Applications exhibit spectral parallelism
  - Parallelism in various levels of granularity
When the applications and the numerical algorithms are simple parallelism can be migrated to a single layer
  - Stencil based finite difference codes
Complex applications discretized by efficient numerical algorithms prevents such migration of parallelism

---
Spectral parallelism
Program level parallelism
  - Optimization of GE solvers
  - Coupled multi-physics solvers
  - Replica exchange
Task level parallelism
  - Domain decomposition
Thread level parallelism
  - Functional parallelism
Instruction level
vector/pipelined parallelism

---
Mapping of Application parallelism
Data parallelism => task parallelism
  - Each subdomain to a different task
  - Each task perform similar/identical instruction sequence
Code parallelism => thread parallelism
  - Each term in the PDE to a different thread
  - Each thread perform dissimilar instruction sequence
Data parallelism => thread parallelism
  - Poor sustained node performance
  - This is why OpenMP performance is poor in general
Code parallelism => task parallelism
  - Load imbalance issues

---
Balanced system architecture
Two extremes
  - Millions of fine grained nodes
  - One large global shared cache coherent shared memory node
Petascale system based on a reasonable size node

---
Node design
¼ to ½ the no. of cores/processors can saturate node's memory, Interconnect, IO bandwidths
Code/functional parallelism is ideal to map within a node
Data parallelism is ideal to map across nodes
Asynchronous parallelism is key to extracting best sustained node performance

---
PGAS languages
MPI-1 forces synchronousness
Often synchronization and communication are combined
PGAS languages: Natural way to express asynchronous parallel programming
Our petascale architecture provides native support to PGAS languages and libraries.

---
Computational Characteristics
GEs dictate whether a problem is
  - Tightly coupled or loosely coupled
  - Compute intensive,
  - Memory intensive,
  - Communication intensive, or,
  - IO intensive
At zeroth order HPC application can be characterized by its compute, memory, communication and IO characteristics.
One can derive computation/communication ratio of a given problem from GEs: FLOPS/Bytes

---
Sustained Performance really matters little

---
Over all Simulation Efficiency
For a given problem size and given solution accuracy, time to solution
This is a product of numerical efficiency, sequential and parallel efficiencies
Code with very high sustained FLOPS and poor numerical efficiency will have poor time to solution

---
Balance
Memory Bandwidth
[ Bytes/sec ]
Interconnect Bandwidth (B/s)
I/O
[ Bytes/sec ]
[ Bytes/sec ]

---
SUN's HPC hardware Strategy
We traverse the 3D HPC space by changing
The ratio of cores to DIMMs and speed of memory bus
the node size vs the number of HCAs
Ratio of compute nodes vs supporting IO nodes
Design target is towards a balanced system than a targeted benchmark system

---
Balance Ratios
Bytes/FLOPS memory: 0.25 to 0.5
Bytes/s/FLOPS memory BW: 0.25 to 0.5
Bytes/s/FLOPS Interconnect BW: 0.025 to 0.05
Bytes/FLOPS Disk capacity: 10 to 20
Bytes/s/FLOPS Disk BW: 0.0005 to 0.002

---
SUN's HPC Strategy
Infusion of
innovation
Arms race
Petaflops
Custom solution
~50 TFLOPS
Semi-Custom
1 to 2 Racks
Standard product

---
Infusion of Innovation at the high end
Hardware and software research and development plans till 2011
Driven by HPCS and various Petascale initiatives
Innovation at processor level as well as system level
ROCK processor based
X86_64 commodity processor based
Node designs with high sustained performance
Ultra dense reliable storage nodes

---
Commodity processor based
Adopt best commodity components and innovate in the Glue space to achieve best price/performance
Be non-religious
  - Sometimes it is hard
  - Short term economic
  - Company egos etc.

---
Typical HPC Center/ Data Center
Login Nodes
 Compute
Resource
 Compute
Resource
Meta
data
Compute Nodes
Mgmt
node
SMP
Thumper
node
 IB Switch
Lustre / DQ FS
Nearline Archive
Test System(s)
Enterprise Storage
(SAM-QFS)
Visualization
Network
Data
Mover

---
Legend
Redundant with fail over capability
  - LN: Login Nodes
  - MN: Management Nodes
  - MD: MetaData Servers
TN: Thumper Nodes
CN: Compute Nodes
SMP (optional): Opteron or SPARC SMP system
All nodes are connected with 10/100, GigE and IB

---
Hurdles to sustained petaflops Performance
RAS, fault tolerance and check pointing
Very poor single node performance
OS jitter and scaling
Programmability, Performance analysis, scalable tools
Environmentals
  - power,space,cooling

---
Magnum System: Key technologies
Fault tolerance and System-wide RAS features
System initiated check pointing
PGAS languages, Fortress
Performance analysis and productivity tools
Support for multiple parallel paradigms
Support for dynamic application specific OS booting
Support for dynamic fine grained power management

---
Magnum RAS features
ECC-Chip-Kill protected memory
  - Can auto-correct memory errors
Minimization of movable parts
  - Leaf switches
  - Drastic reduction of number of cables
Redundant power supplies, fans, and dual  disks with hardware RAID
All nodes contain Service processor
Multiple interconnect paths
Predictive analysis of failures

---
Magnum RAS
Dual login nodes, dual management nodes, dual MDS nodes with fail over
Raid 6 with in a OSS (Object Storage Server)
LAID across OSSs
Separation of data and meta-data

---
MAGNUM RAS
Software RAS
  - Diskless management of compute nodes
  - System initiated check pointing by 09/10 time frame
  - Fault tolerant MPI
  - Strict resource controls on the node by resource manager
  - Bringing the node to neutral state after each job

---
Magnum sustained node performance
Provide hardware and software support for truly asynchronous programming
Extra resources for message handling
  - computation/communication overlap
Extra resources for handling OS tasks
Key to better node performance is to spread the requests (stress) on memory, interconnect and IO
Work with application teams to convert/develop asynchronous parallel programs

---
OS Jitter
Minimize OS jitter through
  - Dedicated resources for system tasks and message handling
  - Clean Kernel
Make application immune to it by asynchronous programming model
Separation of communication and synchronization

---
Programmability, scalable tools
Support of several communication protocols
  - Message passing
  - PGAS languages
Much more easier to implement
  - high level efficient libraries like Charm++, Global Arrays
  - High level languages: UPC, Co-array Fortran
SUN's Fortress language
Leverage SUN's HPCS investments

---
Programmability, scalable tools
Can use HPCS (from SUN Labs) developed performance analysis, modeling tools
Support both user and system initiated checkpointing
  - To other node's memory
  - To disk

---
Magnum: Environmentals
Extremely Dense system design
  - 10s of Teraflops per rack
Innovative cooling techniques
  - Can extract upto 100KW per rack
Efficient dynamic fine grained power management
  - Scheduler based suspension of sockets, nodes
  - 20 to 40% power savings

---
SUN's HPC Strategy: IO, Storage
Wide range of storage solutions
SATA
Fiber-Channel
Intelligent storage called Thumper
High speed parallel file system
Parking storage
Permanent archive tape storage
Wide range of SANs and filesystems
Acquired Storagetek

---
SUN's HPC Software Strategy

---
HPC Software Strategy
Open source, Open standards
Support OpenSolaris and Linux HPC software stack
Open source + SUN developed components + SUN’s partner provided
Complete ownership of the whole stack and the support issues
Several of the SUN’s stack can co-exist, interoperate with third party software components

---
SUN's Software Stack
Java/Grid toolkit
Parallel Debug., Perf. Tools, libraries
N1GE Resource Scheduler
PBS, MOAB etc.
N1SM Cluster management
Rocks, Oscar etc
SUN Studio Compilers
Pathscale, PGI
Cluster File System
SUN Cluster Tool Kit
OpenIB, OpenMPI
Linux
Solaris
SPARC
Opteron

---
Sun and InfiniBand
Sun an original driver of InfiniBand
  - Sun/Intel collaboration, driving the IB specification
  - A founder of OpenFabrics (formerly OpenIB)
InfiniBand is fundamental part of Sun products
  - Performance via high bandwidth and low latency
  - Remote Direct Memory Access (RDMA) critical to HPC
Strong supporter of industry standard IB for Linux
Support for all major IB providers
  - Voltaire, Cisco/Topspin, SilverStorm, Mellanox, QLogic/PathScale

---
Sun Open MPI
Sun has joined Open MPI with the firm belief that HPC ultra-scale MPI computing requirements are best met through a concerted and collaborative effort for the good of the community as a whole.
Open MPI brings together world-class expertise to deliver ultra-scale MPI capabilities
Sun engineers will be active developers of Open MPI
Sun brings nine years of MPI experience with extensive thread-safety and shared-memory communication expertise (former Thinking Machines Globalworks team)
Sun Open MPI: tested and supported to Sun's level of quality

---
Other Upcoming Capabilities
ROCKS port of Solaris
Ubuntu Linux on SPARC
Xen virtualization (hypervisor) for Solaris
  - Open source technology allowing multiple operating systems to run simultaneously on a single system
  - Can migrate an OS environment to another hardware system easily with almost no downtime
  - Prototype running today
[Speaker Notes: As the number of systems grow in any organization, the complexities of managing this infrastructure through its lifecycle becomes increasingly apparent. A server could see many re-provisions applied to it in its lifetime:. Once provisioned, organizations must continuously monitor and manage the infrastructure to ensure that systems are running at desired levels. Managing each step of the infrastructure lifecycle is challenging for even the most sophisticated IT organizations. Sun N1 System Manager helps customers address these problems with its new infrastructure lifecycle management software. Designed specifically to address the problems associated with managing infrastructure throughout its lifecycle, N1 System Manager helps customers provision, monitor, and manage Sun x64 servers. N1 System Manager will expand in breadth of HW coverage over time to encompass current and future Sun systems.]

---
Sun and DARPA HPCS Program
Multi-year petascale program from DARPA
Sun, IBM, and Cray down selected in Phase 2
  - Selection of one or two winners imminent
Sustained petaflop target by 2010
Key DARPA goal is High Productivity
High leverage model, driving capabilities into mainstream products for long-term viability
Total redesign from bottom-up of both HW and SW
  - Solaris HPC roadmap for petascale computing

---
Future: Tuned OS
Collaborative agreements with Redhat and Suse
Looking into
  - ways to provide tuned kernel + OS containing necessary drivers specific to front end, management, IO and compute nodes
  - provide tuned kernel configured for HPC workload
  - Memory and processor affinity
  - High priority to compute process
  - Minimal set of daemons and compact memory footprint
  - Large page support

---
Future: productivity and Usability
Hardware support for MPI-2 one sided
Hardware support for libraries like GAs, Charm++
Support for PGAS languages like UPC, CAF
Expected to sustain higher percentage of peak FLOPS

---
Partnerships: system software
Developing partnerships with academic institutions developing performance tools
  - PAPI and ATLAS libraries
  - TAU, DIMMEMAS, Paraver profile/trace tools
  - Goto LAPACK library

---
Towards Petascale system: Current status
Tokyo-Tech with 10k cores
Just won the NSF track 2 system 400TFLOPS +
Several commercial HPC bids in various stages
  - Manufacturing, Oil & Gas, Data centers
Some discussions with various centers for the petascale system

---
PGAS programming model
NSF recognizes the importance of PGAS languages
Co-array Fortran may be part of 2008 Fortran standard
UPC is gaining rapid acceptance
PGAS libraries like GAs, charm++ are becoming critical for petascale science and applications
We plan to support PGAS natively in hardware/software
Native support for MPI-2 one sided communication

---
Rapid absorption of HPCS research
We expect to see several of the technologies developed as part of HPCS work
Some preliminary work in the system initiated check point restart area
Some performance analysis tools developed in the SUN labs as part of HCS work